## Slide 1
Probabilistic
Seismic Hazard & Fragility Analysis
Hands-on: Matlab Tutorials
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
https://github.com/kia13nn/ISPS.git

## Slide 2
Course outline:
Introduction
  PBEE overview
  the PEER-PBEE framework
Probabilistic Seismic Hazard Model
  Concept and Formulation
  Hazard Computation (MatLab)
Vulnerability and Fragility Analysis
  Concept and Formulation
  Fragility Computation (MatLab)
References
http://zonesismiche.mi.ingv.it/
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 3
Introduction
Performance Based Earthquake Engineering
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
https://github.com/kia13nn/ISPS.git

## Slide 4
Probabilistic framework for (i) assessing design, (ii) evaluation and (iii) planning of civil system.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Fig.1 – PBEE concept: seismic performance objectives vs seismic hazard level. ©Poland et al.,(1995)-Vision 2000: Performance Based Earthquake Engineering of buildings. Structural Engineers Association of California, Sacramento, CA.
PBEE: Performance Based Earthquake Engineering
load-and-resistence-factor design (LRFD)
performance based design (PBD):
3Ds – i.e. downtime, dollars, death
2 axes define the domain of acceptable system’s response:
System performance objectives
Seismic hazard level, w.r.t. return periods

## Slide 5
PEER ~ Pacific Earthquake Engineering Research center – analytical approaches based on total probability theorem for the yearly mean numebr of events of a selected decision variable
with the underlying assumptions of:
- Markovian structure  ;
- No-aging effects on structures;
- Poisson’s processes  memoryless seismic events.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
The PEER-PBEE Framework

## Slide 6
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
The PEER-PBEE Framework
where
is an intensity measure (e.g., peak ground acceleration, spectral acceleration, etc.);
is an engineering demand parameter (e.g., interstorey drift);
is a damage measure (e.g., minor, medium, extensive, collapse);
is a decision variable (e.g., monetary losses, fatalities, etc.);
is the mean annual rate of events exceeding a given threshold for a given variable
is the conditional complementary cumulative distribution function (CCDF)

## Slide 7
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
The PEER-PBEE Framework
(i) hazard analysis
(ii) fragility analysis
(iii) damage analysis
(iv) loss analysis

## Slide 8
Probabilistic Hazard Analysis
Formulation and MatLab Computation
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 9
Seismic Hazard Analysis
SHA is the basis for many earthquake design codes and for seismic risk analysis of civil systems.
Useful definitions:
seismic hazard := the exceedance (or occurrence) probability for a given ground motion intensity measure threshold, site and time interval
seismic risk:= the exceedance (or occurrence) probability for a given loss threshold, site and time interval.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 10
DSHA
Evaluate the worst-case scenario
PSHA
Evaluate the exceedance probability of a given g.m. IM threshold at given site and time interval
Seismic Hazard Analysis – DSHA vs PSHA
Four steps of a DSHA and PSHA analyses - Kramer, 1996
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 11
PSHA
Probabilistic Seismic Hazard Analysis (PSHA) evaluates the exceedance (or occurrence) probability of a given ground motion intensity measure threshold at given site and time interval.
PSHA provides a framework in which uncertainties, typically include magnitude size, earthquake location, soil condition, and rate of occurrence of earthquakes, are quantified.
The calculation of seismic hazard is based on the Total Probability Theorem*
<< the probability that a fixed value of ground motionis exceeded at a given site, given the occurrence of random earthquake from the seismic source >>
*see Notes at the end of Presentation
(1)
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 12
PSHA - Steps
i. Source Characterization: Identification and classification of the Ns source  Definition of
ii. Earthquake Size: for each source based on magnitude recurrence relationship
iii. Ground Motion Estimation: empirical regression models named ground motion prediction equations (GMPE)  Definition of
iv. Hazard Computation: solution of the integral (1)
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 13
PSHA – Assumptions:
Eq. (1) is based on the following assumptions:
Earthquakes form a stochastic process;
Earthquakes can be considered instantaneous events and memory-less
the occurrence of earthquakes can be defined as Homogeneus Poisson Process (HPP)
PDF
CDF
exponential distribution of earthquake recurrence
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 14
PSHA – Step 1: Earthquake source characterization
Goal: to identify
Fault sources: individual or multiple identified faults
Area sources: defined by polygons in which seismicity is assumed uniform
(Identification based upon the interpretation of geological, geophysical and seismological – historical data)
and to characterize seismic sources
Point source
Linear source
Area source
(the geometry of the source is used to identify the probability distribution of source-to-site distances)
SOURCES
DISTANCES
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 15
PSHA – Step 2: Earthquake size (Recurrence law)
Goal: to define distribution of
the chance of an earthquake of a given size occurring anywhere inside the source during a specified period of time
The Gutenberg-Richter law (G-R law) expresses the relationship between the magnitude and rate of cumulative number of earthquakes in any given region:
logarithm base 10 of the mean annual rate of exceedance of magnitude , overall rate of earthquakes of the source and relative ratio of small vs large magnitudes
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 16
PSHA – Step 2: Earthquake size (Recurrence law)
Observations:
linked to the minimum magnitude capable of causing damages and to physically capability of seismic zone to generate magnitude with these values
G-R law bounded
given a seismic source, parameters are estimated through statistical analysis of historical data with constraints from geological evidence
paramount aspect regarding completeness and undistortion of the reference catalogue in terms of intensity/magnitude range and time intervals
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 17
PSHA – Step 2: Earthquake size (Recurrence law)
Observations:
http://legacy.ingv.it/roma/attivita/pererischio/macrosismica/Seismic/seismic.html
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 18
PSHA – Step 3: Ground motion predictive equations (GMPE)
Goal: estimate ground motion at the site
Identify the of interest for the situation and purposes;
Estimation of the PDF of the selected by referring to predictor variables such as the earthquake source properties
GMPEs are usually adopted to evaluate the probability that a particular exceeds a certain value, , for a given earthquake , occurring at a given distance,
Schematic illustration of conditional probability of exceeding a particular value of a
ground motion parameter for a given magnitude and distance.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 19
PSHA – Step 3: Ground motion predictive equations (GMPE)
In probabilistic terms
Usually, the conditional distribution of the ground motion intensity measure, i.e. is assumed log normal.
Observations:
GMPEs are developed independently for each region;
Faulting mechanism, effects of local site conditions are of
paramount importance
Schematic illustration of conditional probability of exceeding a particular value of a
ground motion parameter for a given magnitude and distance.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 20
PSHA – Step 4: Hazard Computation
The seismic hazard curve is a function representing the annual frequency of exceeding various levels of ground shaking (i.e. the ) at a specific site. The curve is obtained by integration of the previously three steps over all possible magnitudes and earthquakes locations.
Seismic hazard curves are obtained for individual sources and, then, combined to express the aggregate hazard at a particular site.
Then
Numerically
(2)
(3)
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 21
Probabilistic Hazard Analysis
Formulation and MatLab Computation
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
https://github.com/kia13nn/ISPS.git

## Slide 22
Goal: to perform a PSHA analysis
Through the scheme depicted in (1), compute:
the annual hazard curve for each fault;
the 50 years hazard curve for each fault;
the 475 years hazard curve for each fault
for the highlighted seismic site.
http://esse1-gis.mi.ingv.it/
Seismic hazard map: shaking parameter PGA, site Palmoli (CH) Latitude 41,527 – Longitude 14,483.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 23
Step 1: Source characterization
Localize seismogenetic zones: Italian ZS9* model for application of the attenuation law
Different characteristics of zonation by:
Seismogenetic faults and mechanisms (direct, inverse, strike-slip …)
Hypocenter depth (shallow, intermediate, deep)
ect.
Italian database and catalogue of the overall seismicity
http://zonesismiche.mi.ingv.it/
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 24
Step 1: Source characterization
Localize seismogenetic zones: Italian ZS9* model for application of the attenuation law
http://zonesismiche.mi.ingv.it/
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 25
Step 1: Source characterization
Extrapolate information regarding the source and its bound limits: convert coordinates from deg2utm for each sources
 | Coordinates |  |  |  | 
 | WGS 84 |  | UTM |  | UTM-Z
Location | long (x) | lat (y) |  |  | 
Palmoli | 14,48 | 41,63 | 465.293 | 4643124 | 33 T
Source | b | Mw Max | Mw Min | Rate
S1 | -1,11 | 6,37 | 4,76 | 0,21
S2 | -1,09 | 7,06 | 4,76 | 0,14
… | … | … | … | …
ZS9-918 | S1 |  |  |  |  | 
WGS 84 |  | UTM |  | UTM-Z | UTM-INPORT | 
12,11651 | 43,79397 | 268015,9 | 4853032 | 33 T | -197.277 | 209.907
12,27012 | 44,10645 | 281523,5 | 4887320 | 33 T | -183.769 | 244.196
13,54116 | 43,2943 | 381660,3 | 4794530 | 33 T | -83.633 | 151.405
14,181 | 42,47483 | 432678,9 | 4702824 | 33 T | -32.614 | 59.699
14,37249 | 42,14993 | 448153,3 | 4666614 | 33 T | -17.140 | 23.489
14,27923 | 41,85719 | 440174,4 | 4634171 | 33 T | -25.118 | -8.953
13,1518 | 43,02822 | 349423 | 4765606 | 33 T | -115.870 | 122.481
12,11651 | 43,79397 | 268015,9 | 4853032 | 33 T | -197.277 | 209.907
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 26
Step 1: Source characterization - Location
Define the distribution of
To simplify, consider 1 source with a regular zonation of .
So, the distribution of an epicenter being located at a distance of less than r is:
CDF:
PDF:
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 27
Step 1: Source characterization
Codes:
Read source.xls file
Run section Earthquake source characterization in the attached Matlab code or load variable seismic_source.mat already prepared with the previously seen data
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 28
Step 1: Source characterization - Location
Codes:
% PDF of R
rmax = Rmax*100; % 50km
rmin = Rmin.*100; % site
r_step = R_step;
r = rmin:r_step:(rmax-r_step);
Fr = r.^2./rmax.^2;
fr = 2*r./rmax.^2;
DFr = r_step;
frdiscr = zeros(1,numel(Fr));
Frdiscr = zeros(1,numel(Fr));
for idr = 2:numel(Fr)
frdiscr(idr) = -(Fr(idr-1)-Fr(idr))./(DFr);
Frdiscr(idr) = Frdiscr(idr-1)+Fr(idr);
end
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 29
Step 2: Earthquake size
Define the distribution of
Gutenberg-Richter bounded defines the relationship between the magnitude and rate of cumulative number of earthquakes
)
CDF:
PDF:
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 30
Step 2: Earthquake size
Define the distribution of : Discretize
Converting the continuous distribution of magnitudes into a discrete set of magnitudes holds
where are the discrete set of magnitudes ordered so that
Codes:
% PDF of M
Nm = 1000; % No. of discretized points between m0 and mu for numerical integration
M = linspace(m0,mu,Nm); %mo = m_min
fM = beta*exp(-beta*(M-m0))/(1-exp(-beta*(mu-m0)));
dM=M(2)-M(1);
Mdiscr=fM*dM;
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 31
Step 3: Ground motion estimation
Define effects : Attenuation models or prediction models
These models predict the probability distribution of ground motion intensity, as a function of many predictor variables such as the earthquake’s magnitude, distance, faulting mechanism, the near-surface site conditions, etc.
To describe this probability distribution, prediction models take the following general form:
where
is the natural log of the ground motion intensity measure of interest;
is modeled as a random variable and is represented by a normal distribution;
and are the predicted mean and standard deviation of ;
and are functions of the earthquake’s magnitude , distance and other parameters
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 32
Step 3: Ground motion estimation
Define effects : Attenuation models or prediction models
Here, for clarity, it is assumed Cornell (1979) for the mean of log peak ground acceleration (in units of g):
with
of ;
normally distributed
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 33
Step 3: Ground motion estimation
Define effects : Attenuation models or prediction models
We can thereby compute the probability of exceeding any PGA level using knowledge of this mean and standard deviation:
where is the standard normal cumulative distribution function.
N.B.: these probabilities correspond to the fraction
of the corresponding PDFs that are shaded.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 34
Step 3: Ground motion estimation
Define effects : Attenuation models or prediction models
Codes:
function [mean_im, sigma_im] = GMPE(magnitude,R_distance)
%Cornell et al. (1979): Ground motion predictive equation for PGA
mean_lnPGA = -0.152+0.859*magnitude -1.803*log(R_distance+25);
mean_PGA = exp(mean_lnPGA);
mean_im = mean_PGA;
sigma_im = 0.57;
end
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 35
Step 4: Hazard Computation
Combine all information: compute
Compute the probability of exceeding an IM intensity level x, given occurrence of a future earthquake from a single source:
II. Compute the rate of IM > x for each single source:
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 36
Step 4: Hazard Computation
Combine all information: compute
III. Considering all sources by the sum of the rates of IM > x from each individual source, we can write:
where is the number of sources considered, and denote the magnitude ~ distance
distributions for source i
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 37
Step 4: Hazard Computation
Combine all information: compute - Discretize
IV. By discretizing:
where the range of possible and have been discretized into and intervals, respectively
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 38
Step 4: Hazard Computation
Goal and results
Through the scheme depicted in (1), compute:
the annual hazard curve for each fault;
the 50 years hazard curve for each fault;
the 475 years hazard curve for each fault
for the highlighted seismic site.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 39
Step 4: Hazard Computation
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 40
Summary
Location
Poisson model
𝑃=1−𝑒^(−𝜆𝑡) Poisson model
Size
Time
source site distance
𝑓_𝑅 (𝑟) source site distance
GMPE
magnitude distribution
𝑓_𝑀 (𝑚) magnitude distribution
attenuation law
𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟) attenuation law
Location
Size
Time
GMPE
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 41
Fragility Analysis
Formulation and MatLab Computation
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 42
Fragility Analysis
Fragility (or Vulnerability) Analysis is the second step of the PBEE-PEER framework
Useful definitions:
seismic fragility function := the conditional probability of an event given the observation of an intensity measure which describe the seismic event.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 43
The fragility curve is defined as the conditional probability of failure of a structure, or its critical components, at given values of seismic intensity measures (IMs).
In practice, a fragility curve is calculated as the conditional probability that the damage measure (D) exceeds a critical threshold, for a given seismic IM.
Fragility Analysis
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
VULNERABILITY
Vulnerability analysis
engineering demand par.
VULNERABILITY
Damage analysis
damage measure
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 44
INTENSITY MEASURE | DAMAGE STATE
in terms of: Efficiency, i.e. variability of an EDP for a given IM; Robustness, i.e. efficiency between IM-EDP at different period ranges; Practicality, i.e. correlation to known and easy identifiable engineering quantities; Sufficiency, i.e. validity of EDP¦IM as statistically independent from gm site characteristics; Effectiveness, i.e. ability to evaluate an analytical relation. | Should suit the specific structural problem  associate each damage state to a specific EDP Categorical variables, i.e. no damages – minor – ; Probabilistic or deterministic relationship between EDP and D
in terms of: Efficiency, i.e. variability of an EDP for a given IM; Robustness, i.e. efficiency between IM-EDP at different period ranges; Practicality, i.e. correlation to known and easy identifiable engineering quantities; Sufficiency, i.e. validity of EDP¦IM as statistically independent from gm site characteristics; Effectiveness, i.e. ability to evaluate an analytical relation. | 
Fragility Analysis: key aspects
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
VULNERABILITY
Vulnerability analysis
engineering demand par.
VULNERABILITY
Damage analysis
damage measure
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 45
EMPIRICAL | ANALYTICAL | EXPERT OPINION | HYBRID
by fitting a function to observational data from past earthquakes or lab tests collections pairs of level of excitation and categorical variables of damage or collapse | by defining analytical structural model and analyzing its performance under different levels of the seismic hazard static, i.e. hazard as response spectrum and push-over analysis vs dynamic, i.e. collection of gms and simulations on FEM via NLA | by polling one or more experts of the given structural asset to guess or estimate the failure probability for a given hazard level | based on combination of the different methods
Class of fragilities
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 46
Dynamic based fragility functions: steps
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Definition of a numerical model:
Selection of a suitable given the structure
Selection of a suitable set of gms for the location
Selection of an of interest
Definition of damage limit states via thresholds
Scale each gm based on the given eventually until collapse
Save each threshold- pair for each gm
Full IDA
Truncated IDA
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 47
Computation of fragility function
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
FULL IDA | TRUNCATED IDA
damage state results, since reached the given damage state where is the CDF of the normal distribution and | upper limit; data that causes collapse , data that do not cause collapse a) b) a)+b)
FULL IDA | TRUNCATED IDA
Hp: - assume a lognormal probabillity distribution for the random variable associated with given
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 48
Computation of fragility function
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
TRUNCATED IDA
TRUNCATED IDA
The likelihood for the entire set of data
And the log likelihood
Estimation of parameters by optimization
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 49
Computation of fragility function
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
For a generic
And the log likelihood
Estimation of parameters by optimization
Fig.1 – Fragility function computed via IDA, see Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 50
Fragility Analysis
Formulation and MatLab Computation
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 51
Goal: to perform fragility analysis
Given the provided set of ground motions, perform a classical and truncated incremental dynamic analysis (IDA) and determine fragility curves for:
ATTEL – moment resistant frame (MRF);
ATTEL – braced frame (BF)
by considering both
Linear elastic behaviour
Bouc – Wen model for hysteresis
3D model of the case study ATTEL – SERA project.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 52
Main steps:
Definition of the numerical model
Input and IM selection
Definition of damage limit states and reference EDP
Performing non-linear time histories analysis (IDA, truncated IDA, cloud, MSA …)
Collecting results pairs and computing fragility
3D model of the case study ATTEL – SERA project.
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 53
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
T1 = 2,79 s
T1 = 0,46 s
[1]BURSI, PUCINOTTI, TONDINI, ZANON, Tests and model calibration of high strength steel tubular beam-to-column and column-base composite joints for moment-resisting structures, Earthquake Engineering and Structural Dynamics, (2015).
3D model of the case study ATTEL – SERA project.
Step 1: the case study ATTEL(1)
Main sections of the moment resistent frame and the braced one.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 54
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Designed according to EC8 and modelled in OS:
beam and column elements with linear elastic behavior
mechanical nonlinearities
geometric nonlinearities
Model of the structure in OpenSees.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: Le strutture, progettate secondo criteri e norme antisismiche, sono state modellate dettagliatamente prima in OpenSees, software opensource sviluppato a Berkeley per l’analisi strutturale e geotecnica agli elementi finiti. Il modello, sviluppato in un precedente lavoro di tesi magistrale degli ingegneri Fassin ed Eccher, è stato realizzato mediante l’utilizzo di elementi elastici lineari BeamColumn, concentrando invece le non linearità meccaniche nelle c.p., considerando un modello isteretico di BW e fenomenologico di pinching calibrato sperimentalmente sui dettagli costruttivi dei giunti, oggetto di altri lavori di tesi. Sono state inoltre considerate le non linearità geometriche mediante gli effetti P-Delta.
λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 55
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
to reduce computational burden
to reduce required simulation times
high fidelity model in OpenSees - OS
simplified model MDOF in MATLAB ® - ML
High number of analysis
for seismic simulations
Calibration oriented to correspondence of:
main periods
modes of vibrating
dissipative behavior
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: Viste però le numerose analisi e simulazioni richieste per la stesura del modello probabilistico, è stato necessario passare da una struttura complessa ad una MDOF più semplice per motivi di onere computazionale e tempi di analisi impiegati. Si è svolta pertanto una procedura di calibrazione volta alla corrispondenza di periodi principali, modi di vibrare e comportamento dissipativo.

## Slide 56
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Hysteretic model of Bouc Wen.
Formulation of the problem and examples of hysteretic cycles.
Hysteretic model of Bouc Wen
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Notes: In particolare nella condensazione della struttura al modello in ML si è prestata specifica attenzione al comportamento isteretico, sviluppando un apposito modello di Bouc-Wen per tenere in conto della risposta in campo non lineare associata al degrado in termini di resistenza e rigidezza della struttura.
Peculiarità del modello isteretico risiede nel definire la Fs forza di richiamo come il contributo di due termini in parallelo: il primo rappresentante un contributo elastico, il secondo il contributo dissipativo.

## Slide 57
Step 2: input and IM selection
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Acceleration, velocity and displacement response spectra with mean value, 10-th and 90-th quantile.
Scatter plot for correlation.
Data exploration of recorded gms
Scatter plot and statistic tools to evaluate proper IM
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 58
Step 2: input and IM selection
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Codes:
%% Ground motions
Ground_motions = load('accelrot_cellarray.mat');
%
NN = [1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 16, 17, 19, 21, 23, 24,...
25, 26, 28, 29, 30, 31, 32, 33, 34, 36, 37]; % number ID of the SS ground motions
DT = [0.01 , 0.01 , 0.005, 0.005, 0.005, 0.005, 0.02 , 0.02, 0.02, 0.01,...
0.01 , 0.01 , 0.02 , 0.02 , 0.02 , 0.02 , 0.02 , 0.02, 0.01, 0.01,...
0.005, 0.005, 0.005, 0.005, 0.02 , 0.005, 0.005, 0.01, 0.01, 0.01,...
0.01 , 0.005, 0.005, 0.02 , 0.005, 0.01 , 0.01]; % integration time step
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 59
Step 3: Definition of damage limit states and reference EDP
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Document FEMA 356 - Prestandard and Commentary for the Seismic Rehabilitation of Buildings; Table C1-3 - Structural Performance Levels and Damage.
MRF
BF
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 60
Step 3: Definition of damage limit states and reference EDP
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Codes:
%% MDOF Properties
% Choose between the structural system
MDOF_properties_BW_MRF
MDOF_properties_BW_BF
% and between linear or hysteretic behaviour
%% Structural behaviour
System_type = ‘le’; % ‘bw’
% bw = bouc-wen
% le = linear elastic
…
%% Limit States
LS = [0.50 0.75 1 2 3]*4/100;
for ls_i = 1:numel(LS)
ls_val = LS(ls_i)
Main_IDA_o_t
ls_i = ls_i + 1;
end
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 61
Step 4: Performing non-linear time histories analysis
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Codes:
%% Initial condition
Mat.dFe=zeros(Mat.NDOF,numel(a_g_norm)); % Preallocation for the load for the time series
a_g = a_g_norm*scale; % Scaled ground motion
Mat.Fe=Mat.M*Mat.r'*a_g'*g;
%% Computation response
[HistVarBw]=ResponceMDF_Bw(Mat);
edp = max(abs(HistVarBw.eps(1,:)));
EDP(i) = edp; %store the EDP for each time history analysis
SCALE(i) = scale; %store the scale factor for each time history analysis…
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 62
Step 5: Computing fragilities
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Codes:
%% Untruncated IDA
[parmhat,parmci] = lognfit(IM_t_c ,0.01);
mu_IDA = parmhat(1);
sigma_IDA = parmhat(2);
%% Truncated IDA
IM_max = 2.2;
IM_trunc = IM_t_c(IM_t_c < IM_max); % take only the results with IM < IM_max
eq_over = sum(IM_t_c >= IM_max); % number of analyses reached IM_max without collapsing
% Maximum likelihood fit, using equation (1) and (2) of previously slides
[mu_IDA_t, sigma_IDA_t ] = truncated_ida(IM_trunc, IM_max, eq_over);
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 63
Step 5: Computing fragilities - Results
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References

## Slide 64
References
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 65
References:
Baker J. W. (2008). An Introduction to Probabilistic Seismic Hazard Analysis (PSHA), White Paper, Version 1.3, 72 pp.
Kramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
Wells, D.L. and Coppersmith, K.J. (1994) New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement. Bull. Seism. Soc. Am., 84, 974-1002.
Cornell, C.A. (1968). Engineering seismic risk analysis, Bull. Seism. Soc. Am., 58, 1583-1606.
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Stucchi M., Meletti C., Montaldo V., Akinci A., Faccioli E., Gasperini P., Malagnini L., Valensise G. (2004). Pericolosità sismica di riferimento per il territorio nazionale MPS04. Istituto Nazionale di Geofisica e Vulcanologia (INGV). https://doi.org/10.13127/sh/mps04/agKramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
http://zonesismiche.mi.ingv.it/  Italian database
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References