## Slide 1
Probabilistic
Seismic Hazard & Fragility Analysis
Hands-on: Matlab Tutorials
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 2
Course outline:
Introduction
  PBEE overview
  the PEER-PBEE framework
Probabilistic Seismic Hazard Model
  Concept and Formulation
  Hazard Computation (MatLab)
Vulnerability and Fragility Analysis
  Concept and Formulation
  Fragility Computation (MatLab)
References
http://zonesismiche.mi.ingv.it/
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 3
Introduction
Performance Based Earthquake Engineering
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 4
Probabilistic framework for (i) assessing design, (ii) evaluation and (iii) planning of civil system.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Fig.1 – PBEE concept: seismic performance objectives vs seismic hazard level. ©Poland et al.,(1995)-Vision 2000: Performance Based Earthquake Engineering of buildings. Structural Engineers Association of California, Sacramento, CA.
PBEE: Performance Based Earthquake Engineering
load-and-resistence-factor design (LRFD)
performance based design (PBD):
3Ds – i.e. downtime, dollars, death
2 axes define the domain of acceptable system’s response:
System performance objectives
Seismic hazard level, w.r.t. return periods

## Slide 5
PEER ~ Pacific Earthquake Engineering Research center – analytical approaches based on total probability theorem for the yearly mean numebr of events of a selected decision variable
with the underlying assumptions of:
- Markovian structure  ;
- No-aging effects on structures;
- Poisson’s processes  memoryless seismic events.
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
The PEER-PBEE Framework

## Slide 6
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
The PEER-PBEE Framework
where
is an intensity measure (e.g., peak ground acceleration, spectral acceleration, etc.);
is an engineering demand parameter (e.g., interstorey drift);
is a damage measure (e.g., minor, medium, extensive, collapse);
is a decision variable (e.g., monetary losses, fatalities, etc.);
is the mean annual rate of events exceeding a given threshold for a given variable
is the conditional complementary cumulative distribution function (CCDF)

## Slide 7
Introduction | Probabilistic Hazard Analysis | Fragility Analysis | References
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
The PEER-PBEE Framework
(i) hazard analysis
(ii) fragility analysis
(iii) damage analysis
(iv) loss analysis

## Slide 8
Probabilistic Hazard Analysis
Formulation and MatLab Computation
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 9
Course outline:
Introduction
  Overview and applications
  DSHA vs PSHA
Probabilistic Hazard Model
  Earthquake Source Characterization
  Earthquake Size
  Ground Motion Estimation
  Hazard Computation
Laboratory
http://zonesismiche.mi.ingv.it/
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 10
Introduction Probabilistic Hazard Model Laboratory
Seismic Hazard Analysis
where is an intensity measure (e.g., peak ground acceleration, peak ground velocity, spectral
acceleration, etc.), is an engineering demand parameter (e.g., interstorey drift), is a damage
measure (e.g., minor, medium, extensive, collapse), is a decision variable (e.g., monetary
losses, fatalities, etc.), is the mean annual rate of events exceeding a given threshold
for a given variable , and is the conditional complementary cumulative distribution function (CCDF)
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.
total probability theorem for the yearly mean number of events of a selected decision
variable.
L’approccio proposto fornisce in output delle
misure quantitative della performance dell’edificio, fra cui in particolare una stima delle perdite
causate dall’evento sismico, quali ad esempio i costi di ricostruzione, l’interruzione di servizio
post-terremoto e il numero di vittime causate dal sisma, altresì note come le 3Ds - dollars, deaths,
downtime
livelli di performance sono quindi definiti in funzione di parametri decisionali detti appunto
decision variables - DVs. In generale, le DVs sono a loro volta funzioni di misure del danno
dette measure variables - DM, funzioni esse stesse di funzioni di domanda ingegneristica dette
engineering demand parameters - EDP, dipendenti da parametri di intensity measures - IM.
ogni freccia rappresenta un modello di relazione probabilistica condizionata.
Per esempio, un opportuno modello generatore di IM fornisce opportuni valori di EDP, mentre
un altro modello di danno fornisce vari DM a seconda dell’EDP in ingresso.

## Slide 11
Introduction Probabilistic Hazard Model Laboratory
Seismic Hazard Analysis
SHA is the basis for many earthquake design codes and for seismic risk analysis of civil systems.
Useful definitions:
seismic hazard := the exceedance (or occurrence) probability for a given ground motion intensity measure threshold, site and time interval
seismic risk:= the exceedance (or occurrence) probability for a given loss threshold, site and time interval.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 12
Introduction Probabilistic Hazard Model Laboratory
Seismic Hazard Analysis - Overview
Reliable SHA in order to minimize:
Loss of life;
Property damage;
Social and Economic disruption.
HAZARD
Hazard analysis
intensity measure
PBEE Framework !
Base-ground for:
Seismic-structural design;
Financial-insurance policies;
Emergency-response policies;
Post-earthquake recovery.
https://peer.berkeley.edu/sites/default/files/web_peer10_02_sanaz_rezaeian_and_armen_der_kiureghian.pdf
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 13
DSHA
Evaluate the worst-case scenario
PSHA
Evaluate the exceedance probability of a given g.m. IM threshold at given site and time interval
Introduction Probabilistic Hazard Model Laboratory
Seismic Hazard Analysis – DSHA vs PSHA
Four steps of a DSHA and PSHA analyses - Kramer, 1996
PBEE Framework !
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: SHA is the basis for many earthquake design codes practices and for seismic risk analysis of civil systems.

## Slide 14
DSHA
Deterministic Seismic Hazard Analysis (DSHA) consists in the analysis of a particular seismic scenario. The output is the intensity level of the scenario: the occurrence of an earthquake of specific size at a given location.
Introduction Probabilistic Hazard Model Laboratory
Definition of earthquake source’s geometry and earthquake potential
i. Identification and Characterization of sources
Evaluation of distance between source zone – site of interest
ii. Selection of source to site distance
Generally described in terms of magnitude and distance from site
iii. Selection of master earthquake
Usually described by one or more g.m. parameters.
iv. Hazard Computation
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 15
PSHA
Probabilistic Seismic Hazard Analysis (PSHA) evaluates the exceedance (or occurrence) probability of a given ground motion intensity measure threshold at given site and time interval.
PSHA provides a framework in which uncertainties, typically include magnitude size, earthquake location, soil condition, and rate of occurrence of earthquakes, are quantified.
The calculation of seismic hazard is based on the Total Probability Theorem*
<< the probability that a fixed value of ground motionis exceeded at a given site, given the occurrence of random earthquake from the seismic source >>
Introduction Probabilistic Hazard Model Laboratory
*see Notes at the end of Presentation
(1)
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 16
PSHA - Steps
i. Source Characterization: Identification and classification of the Ns source  Definition of
ii. Earthquake Size: for each source based on magnitude recurrence relationship
iii. Ground Motion Estimation: empirical regression models named ground motion prediction equations (GMPE)  Definition of
iv. Hazard Computation: solution of the integral (1)
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 17
PSHA – Assumptions:
Eq. (1) is based on the following assumptions:
Earthquakes form a stochastic process;
Earthquakes can be considered instantaneous events and memory-less
Introduction Probabilistic Hazard Model Laboratory
the occurrence of earthquakes can be defined as Homogeneus Poisson Process (HPP)
PDF
CDF
exponential distribution of earthquake recurrence
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 18
PSHA – Step 1: Earthquake source characterization
Goal: to identify
Fault sources: individual or multiple identified faults
Area sources: defined by polygons in which seismicity is assumed uniform
(Identification based upon the interpretation of geological, geophysical and seismological – historical data)
and to characterize seismic sources
Point source
Linear source
Area source
(the geometry of the source is used to identify the probability distribution of source-to-site distances)
Introduction Probabilistic Hazard Model Laboratory
SOURCES
DISTANCES
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 19
PSHA – Step 2: Earthquake size (Recurrence law)
Goal: to define distribution of
the chance of an earthquake of a given size occurring anywhere inside the source during a specified period of time
The Gutenberg-Richter law (G-R law) expresses the relationship between the magnitude and rate of cumulative number of earthquakes in any given region:
logarithm base 10 of the mean annual rate of exceedance of magnitude , overall rate of earthquakes of the source and relative ratio of small vs large magnitudes
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 20
PSHA – Step 2: Earthquake size (Recurrence law)
Observations:
linked to the minimum magnitude capable of causing damages and to physically capability of seismic zone to generate magnitude with these values
G-R law bounded
given a seismic source, parameters are estimated through statistical analysis of historical data with constraints from geological evidence
paramount aspect regarding completeness and undistortion of the reference catalogue in terms of intensity/magnitude range and time intervals
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 21
PSHA – Step 2: Earthquake size (Recurrence law)
Observations:
Introduction Probabilistic Hazard Model Laboratory
http://legacy.ingv.it/roma/attivita/pererischio/macrosismica/Seismic/seismic.html
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 22
PSHA – Step 3: Ground motion predictive equations (GMPE)
Goal: estimate ground motion at the site
Identify the of interest for the situation and purposes;
Estimation of the PDF of the selected by referring to predictor variables such as the earthquake source properties
GMPEs are usually adopted to evaluate the probability that a particular exceeds a certain value, , for a given earthquake , occurring at a given distance,
Introduction Probabilistic Hazard Model Laboratory
Schematic illustration of conditional probability of exceeding a particular value of a
ground motion parameter for a given magnitude and distance.
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 23
PSHA – Step 3: Ground motion predictive equations (GMPE)
In probabilistic terms
Usually, the conditional distribution of the ground motion intensity measure, i.e. is assumed log normal.
Observations:
GMPEs are developed independently for each region;
Faulting mechanism, effects of local site conditions are of
paramount importance
Introduction Probabilistic Hazard Model Laboratory
Schematic illustration of conditional probability of exceeding a particular value of a
ground motion parameter for a given magnitude and distance.
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 24
PSHA – Step 4: Hazard Computation
The seismic hazard curve is a function representing the annual frequency of exceeding various levels of ground shaking (i.e. the ) at a specific site. The curve is obtained by integration of the previously three steps over all possible magnitudes and earthquakes locations.
Seismic hazard curves are obtained for individual sources and, then, combined to express the aggregate hazard at a particular site.
Then
Numerically
Introduction Probabilistic Hazard Model Laboratory
(2)
(3)
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 25
References
Baker J. W. (2008). An Introduction to Probabilistic Seismic Hazard Analysis (PSHA), White Paper, Version 1.3, 72 pp.
Kramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
Wells, D.L. and Coppersmith, K.J. (1994) New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement. Bull. Seism. Soc. Am., 84, 974-1002.
Cornell, C.A. (1968). Engineering seismic risk analysis, Bull. Seism. Soc. Am., 58, 1583-1606.
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 26
Ingegneria Sismica e Progettazione Strutturale
PSHA – Assignment 1
Ph.D. Candidate Chiara Nardin – M.Sc., Eng. in Civil Engineering
https://github.com/kia13nn/ISPS.git
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 27
Goal: to perform a PSHA analysis
Through the scheme depicted in (1), compute:
the annual hazard curve for each fault;
the 50 years hazard curve for each fault;
the 475 years hazard curve for each fault
for the highlighted seismic site.
Introduction Probabilistic Hazard Model Laboratory
http://esse1-gis.mi.ingv.it/
Seismic hazard map: shaking parameter PGA, site Palmoli (CH) Latitude 41,527 – Longitude 14,483.
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 28
Step 1: Source characterization
Localize seismogenetic zones: Italian ZS9* model for application of the attenuation law
Different characteristics of zonation by:
Seismogenetic faults and mechanisms (direct, inverse, strike-slip …)
Hypocenter depth (shallow, intermediate, deep)
ect.
Introduction Probabilistic Hazard Model Laboratory
Italian database and catalogue of the overall seismicity
http://zonesismiche.mi.ingv.it/
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 29
Step 1: Source characterization
Localize seismogenetic zones: Italian ZS9* model for application of the attenuation law
Introduction Probabilistic Hazard Model Laboratory
http://zonesismiche.mi.ingv.it/
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 30
Step 1: Source characterization
Extrapolate information regarding the source and its bound limits: convert coordinates from deg2utm for each sources
Introduction Probabilistic Hazard Model Laboratory
 | Coordinates |  |  |  | 
 | WGS 84 |  | UTM |  | UTM-Z
Location | long (x) | lat (y) |  |  | 
Palmoli | 14,48 | 41,63 | 465.293 | 4643124 | 33 T
Source | b | Mw Max | Mw Min | Rate
S1 | -1,11 | 6,37 | 4,76 | 0,21
S2 | -1,09 | 7,06 | 4,76 | 0,14
… | … | … | … | …
ZS9-918 | S1 |  |  |  |  | 
WGS 84 |  | UTM |  | UTM-Z | UTM-INPORT | 
12,11651 | 43,79397 | 268015,9 | 4853032 | 33 T | -197.277 | 209.907
12,27012 | 44,10645 | 281523,5 | 4887320 | 33 T | -183.769 | 244.196
13,54116 | 43,2943 | 381660,3 | 4794530 | 33 T | -83.633 | 151.405
14,181 | 42,47483 | 432678,9 | 4702824 | 33 T | -32.614 | 59.699
14,37249 | 42,14993 | 448153,3 | 4666614 | 33 T | -17.140 | 23.489
14,27923 | 41,85719 | 440174,4 | 4634171 | 33 T | -25.118 | -8.953
13,1518 | 43,02822 | 349423 | 4765606 | 33 T | -115.870 | 122.481
12,11651 | 43,79397 | 268015,9 | 4853032 | 33 T | -197.277 | 209.907
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 31
Step 1: Source characterization - Location
Define the distribution of
To simplify, consider 1 source with a regular zonation of .
So, the distribution of an epicenter being located at a distance of less than r is:
Introduction Probabilistic Hazard Model Laboratory
CDF:
PDF:
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 32
Step 1: Source characterization
Codes:
Read source.xls file
Run section Earthquake source characterization in the attached Matlab code or load variable seismic_source.mat already prepared with the previously seen data
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 33
Step 1: Source characterization - Location
Codes:
% PDF of R
rmax = Rmax*100; % 50km
rmin = Rmin.*100; % site
r_step = R_step;
r = rmin:r_step:(rmax-r_step);
Fr = r.^2./rmax.^2;
fr = 2*r./rmax.^2;
DFr = r_step;
frdiscr = zeros(1,numel(Fr));
Frdiscr = zeros(1,numel(Fr));
for idr = 2:numel(Fr)
frdiscr(idr) = -(Fr(idr-1)-Fr(idr))./(DFr);
Frdiscr(idr) = Frdiscr(idr-1)+Fr(idr);
end
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 34
Step 2: Earthquake size
Define the distribution of
Gutenberg-Richter bounded defines the relationship between the magnitude and rate of cumulative number of earthquakes
Introduction Probabilistic Hazard Model Laboratory
)
CDF:
PDF:
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 35
Step 2: Earthquake size
Define the distribution of : Discretize
Converting the continuous distribution of magnitudes into a discrete set of magnitudes holds
where are the discrete set of magnitudes ordered so that
Introduction Probabilistic Hazard Model Laboratory
Codes:
% PDF of M
Nm = 1000; % No. of discretized points between m0 and mu for numerical integration
M = linspace(m0,mu,Nm); %mo = m_min
fM = beta*exp(-beta*(M-m0))/(1-exp(-beta*(mu-m0)));
dM=M(2)-M(1);
Mdiscr=fM*dM;
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 36
Step 3: Ground motion estimation
Introduction Probabilistic Hazard Model Laboratory
Define effects : Attenuation models or prediction models
These models predict the probability distribution of ground motion intensity, as a function of many predictor variables such as the earthquake’s magnitude, distance, faulting mechanism, the near-surface site conditions, etc.
To describe this probability distribution, prediction models take the following general form:
where
is the natural log of the ground motion intensity measure of interest;
is modeled as a random variable and is represented by a normal distribution;
and are the predicted mean and standard deviation of ;
and are functions of the earthquake’s magnitude , distance and other parameters
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 37
Step 3: Ground motion estimation
Introduction Probabilistic Hazard Model Laboratory
Define effects : Attenuation models or prediction models
Here, for clarity, it is assumed Cornell (1979) for the mean of log peak ground acceleration (in units of g):
with
of ;
normally distributed
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 38
Step 3: Ground motion estimation
Introduction Probabilistic Hazard Model Laboratory
Define effects : Attenuation models or prediction models
We can thereby compute the probability of exceeding any PGA level using knowledge of this mean and standard deviation:
where is the standard normal cumulative distribution function.
N.B.: these probabilities correspond to the fraction
of the corresponding PDFs that are shaded.
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 39
Step 3: Ground motion estimation
Define effects : Attenuation models or prediction models
Introduction Probabilistic Hazard Model Laboratory
Codes:
function [mean_im, sigma_im] = GMPE(magnitude,R_distance)
%Cornell et al. (1979): Ground motion predictive equation for PGA
mean_lnPGA = -0.152+0.859*magnitude -1.803*log(R_distance+25);
mean_PGA = exp(mean_lnPGA);
mean_im = mean_PGA;
sigma_im = 0.57;
end
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 40
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Combine all information: compute
Compute the probability of exceeding an IM intensity level x, given occurrence of a future earthquake from a single source:
II. Compute the rate of IM > x for each single source:
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 41
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Combine all information: compute
III. Considering all sources by the sum of the rates of IM > x from each individual source, we can write:
where is the number of sources considered, and denote the magnitude ~ distance
distributions for source i
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 42
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Combine all information: compute - Discretize
IV. By discretizing:
where the range of possible and have been discretized into and intervals, respectively
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 43
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Goal and results
Through the scheme depicted in (1), compute:
the annual hazard curve for each fault;
the 50 years hazard curve for each fault;
the 475 years hazard curve for each fault
for the highlighted seismic site.
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 44
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 45
Summary
Introduction Probabilistic Hazard Model Laboratory
Location
Poisson model
𝑃=1−𝑒^(−𝜆𝑡) Poisson model
Size
Time
source site distance
𝑓_𝑅 (𝑟) source site distance
GMPE
magnitude distribution
𝑓_𝑀 (𝑚) magnitude distribution
attenuation law
𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟) attenuation law
Location
Size
Time
GMPE
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 46
References
Stucchi M., Meletti C., Montaldo V., Akinci A., Faccioli E., Gasperini P., Malagnini L., Valensise G. (2004). Pericolosità sismica di riferimento per il territorio nazionale MPS04. Istituto Nazionale di Geofisica e Vulcanologia (INGV). https://doi.org/10.13127/sh/mps04/agKramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
http://zonesismiche.mi.ingv.it/  Italian database
Introduction Probabilistic Hazard Model Laboratory
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 47
Total Probability Theorem:
Individual probabilities  Probability Density Function (PDF),
Uniform Distribution Normal Distribution Lognormal Distribution
Probability Theory
See also: https://en.wikipedia.org/wiki/PDF
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it

## Slide 48
Probabilities of exceeding or not exceeding given values i
Uniform Distribution Normal Distribution Lognormal Distribution
Probability Theory
See also: https://en.wikipedia.org/wiki/PDF
Standard Normal CDF
Z-Value
Trento, 09 October 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it